## Slide 1: MANAGING EXTREME WILDFIRES
A virtual PDP Workshop for the 2021 AFAC Conference.
Rick McRae, Jason Sharples
UNSW Bushfire Research Group.
Graphic: Nature.

## Slide 2
INSTABILITY

## Slide 3: Instability/DPD/Cap
Weather balloon (radiosonde) flights provide data on the vertical profile of the atmosphere up to the UTLS.

## Slide 4
Key aspect for BUFE development:
  Purple = Convective cap
  Orange = dew point depression near the cap
  Blue = LCL = cloud base height

## Slide 5: Percentile plots

## Slide 6: BUFE Trend 1
50% of BUFEs occur at or above the 90%ile for all days (3km, equivalent to 20% RH).

## Slide 7: BUFE Trend 2
The 10%ile for BUFEs, 1.5km (equivalent to 40% RH), is the 50%ile for all days.

## Slide 8: PyroCb Trend 1
PyroCbs occur at or above the 90%ile for all days (3km or 20% RH).
PyroCbs mostly occur with low RH and high cloud base.

## Slide 9: PyroCb Trend 2
All pyroCbs occur below the 40%ile CAP.
There is little difference for BUFEs.

## Slide 10: Isentropic drawdown (ID)
Types of foehn wind
Role of ID
  Tathra Fire 20180323
  Northern blocks during BS
[NSWRFS]

## Slide 11
Foehn winds, and especially isentropic drawdown, can drive BUFE development on a large scale.

## Slide 12: Foehn Trend 1
The median LCL height for both foehn BUFEs and foehn events (3km) is double that for all days(1.5km).

## Slide 13: Foehn Trend 2
There is a tendency for foehn BUFEs and, to a lesser extent, foehn winds to occur under stronger CAPs.

## Slide 14: Haines Indices?
Work underway shows that, during BS:
  5% of CH values were correctly based on data from below the LCL.
  60% of CH values were based on data from above the LCL.
  35% of CH values were based on data from either side of the LCL.
CH can either indicate FDR or instability, not both.
BUT both can indicate a BUFE potential.
Note: The LCL values used here are estimated from surface T and DP, as might be done in the field on a bad fire day. On the right are values for measured change points in the T trace.
Data: University of Wisconsin, Analysis: McRae

## Slide 15: Caveat
Technically, Mid-level C-Haines should only be used on a fire day when the RH is less than 12%!
However on bad fire days it “works” for RH up to 25% if there is a DPD in place near the LCL.

## Slide 16: C-Haines Trend
A DPD of 32°C is exceeded by:
  25% of all days
  50% of BUFEs
  75% of pyroCbs

## Slide 17
The role of the convective cap must be understood.

## Slide 18
High country plumes can bounce back off a convective cap and drive unexpected fire runs.
Brian Potter: The Drumskin Effect.

## Slide 19
The role of dew point depression near the LCL must be understood.

## Slide 20
The role of the LCL must be understood.

## Slide 21
Caution is required if using C-Haines as an index for instability.

## Slide 22
An old learning worth repeating: The instability of the atmosphere above the LCL must be understood.

## Slide 23: Undular Bores
These synoptic-scale outflows from storm systems act to reduce the convective cap and can help trigger a BUFE, Cb, or pyroCb.
Undular bores from storms cells, 11 Dec 2016. [H8 imagery, US Naval Research Laboratory, Monterey]